Nanooptics and photonics
Impact of Si nanowires array thickness on small angle elastic backscattering manifestation
V.V. Multian1, A.V. Goncharenko2, P.I. Budnik1, V.Ya. Gayvoronsky1
1 Institute of Physics NAS of Ukraine. Pr. Nauki, 46, Kyiv 03028, Ukraine
E-mail: vlad@iop.kiev.ua
2Institute of Semiconductor Physics NAS of Ukraine, Pr. Nauki, 41, Kyiv 03028, Ukraine

Silicon nanowires (SiNW) arrays are under study for application optoelectronics, photovoltaics and biomedicine. Studied SiNWs arrays were produced by metal assisted wet chemical etching of lightly-boron doped (100)-oriented Si wafers in hydrofluoric acid solution. Such arrays have specific features of optical response: (i) room temperature photoluminescence (PL) in visible and near infrared (IR) spectral regions, (ii) enhanced Raman scattering and (iii) coherent anti-Stokes Raman scattering, (iv) low total reflectance in the visible spectral range.
The impact of SiNW arrays thickness (0.4 – 4.6 μm) on angular redistribution of the elastic scattered light was studied at wavelength of 1064 nm. Experimental setup is described in [1]. The samples with SiNWs exhibit a strong decrease of the total reflectance to 10-14 % in comparison to c-Si substrate (35%). It can be explained by the strong light scattering and absorption, which results in partial localization (trapping) of the excitation light in SiNW arrays. SiNWs arrays on c-Si wafer generally demonstrate a reduction of the scattered signal magnitude in forward hemisphere and in backward direction with a SiNWs length increase.
Within bidirectional reflectance distribution function approach we analyzed impact of SiNWs array thickness on small angle elastic backscattering manifestation in the far field [2]. In the generalized Rayleigh-Gans approximation it was shown that small angle backscattered signal formation can be explained as a superposition of the following contributions: (1) direct scattering from the nanowire; (2) consequent scattering on SiNW and then on substrate; (3) scattering from c-Si substrate.
Acknowledgement. V.M. acknowledges support by the NASU project (grant #0118U002330) for research groups of young scientists.

1. V.V. Multian, V.V. Lisnyak, V.Ya. Gayvoronsky et al. Surface Response of Brominated Carbon Media on Laser and Thermal Excitation: Optical and Thermal Analysis Study. Nanoscale Res. Letters 12 (2017)146 (8 pp.)
2. W. M. Bruno, J. S. Bessey, P. M. Whitesmith et al. Scattering by random particles on optical surfaces. Appl. Opt. 35 (1996) 2292 (12 pp).