Nanocomposites and nanomaterials

Influence of synthetic conditions on structure of nanoporous metal (Cu, Ag) foams and their composites with MOFs
Lytvynenko A.S.1,2, Brzózka A.2, Kurmach M.M.1, Sulka G.D.2, Kolotilov S.V.1
1 Porous Compounds and Materials Dept., L. V. Pisarzhevsky Institute of Physical Chemistry of the NAS of Ukraine. Prospect Nauky, 31, Kyiv-03028, Ukraine.
E-mail: anton.s.lytvynenko@gmail.com
2 Jagiellonian University, Faculty of Chemistry, Gronostajowa 2, 30-387 Kraków, Poland

Nanoporous metal foams (NFs) are a promising kind of nanomaterials for a variety of applications, especially electrocatalytically active electrode coatings [1]. It was previously shown by us [2] that Ag NFs exhibited superior electrocatalytic activity in reductive dehalogenation of organic halides compared to smooth silver. Variation of NFs structure as well as their superficial modification by microporous substances such as metal-organic frameworks (MOFs) can allow further improvement of NF activity. The aim of this work was to elucidate the influence of synthetic conditions on the structure of NFs as well as to evaluate possibility of preparation of NF-MOF composites using preliminary synthesized MOF powders.
The NFs were synthesized by electrodeposition from acidic solutions of the metals salts [1,2] varying concentrations of the metal ion and the acid, deposition time and current density (or potential). Modification of the NFs by MOFs (HKUST-1, MIL-53-FA(Al) etc.) was provided by dropcasting of the MOFs par­ticle suspension. The only factor notably impacted the morphology of Ag NF was Ag+ concentration (its increase led to increase in size of NF structural elements). NF-MOF composites exhibited unexpected stability to washing MOFs particles out by solvents, probably due to intercalation (revealed by SEM) of the particles between NF filaments caused by surface tension forces upon solvent drying.
The work was co-financed by the Governments of Czechia, Hungary, Poland and Slovakia through Visegrad Scholarship from International Visegrad Fund granted to A.S.L. in 2018 (contract number 51810453).

1. Sen S., Liu D., Palmore G. T. R. Electrochemical Reduction of CO2 at Copper Nanofoams // ACS Catal.-2014.-4.-P. 3091-3095.
2. Mishura A.M., Lytvynenko A.S., Gavrilenko K.S., Baranchikov A.E., Gra­bovaya N.V., Kiskin M.A., Kolotilov S.V. Formation of hierarchically-ordered nanoporous silver foam and its electrocatalytic properties in reductive dehalo­genation of organic compounds // New J Chem.-2018.-42.-P. 17499-17512.