Nanoplasmonics and surface enchanced spectroscopy

Modulating plasmon properties of silver nanoparticles in liquid crystal assemblies
Jarmuła P.1, Grzelak D.1, Lewandowski W.1
1 Laboratory of organic nanomaterials and biomolecules, Faculty of Chemistry, University of Warsaw, Pasteura 1, 02-093 Warsaw, Poland.
E-mail: p.jarmula5@gmail.com
Precise control over plasmonic properties of metallic nanoparticles is of utmost importance for future metamaterial-based technologies. Such control can be achieved by functionalizing nanoparticle surface with various liquid crystal ligands. Most interesting structures obtained this way include hybrid materials with reversibly switchable optical properties [1]. In my research I am trying to obtain such materials with as perfect plasmonic properties as possible with as big plasmon band shift with temperature change as possible.
 Up to this point hybrid, liquid crystalline nanoparticles were obtained from nanocrystals with diameter below 5 nm, for which plasmon intensity is relatively weak. Optimization of plasmonic properties can be achieved by increasing the size of nanoparticles up to 20 nm, by reducing the number of multi-twinned nanocrystals or by increasing their monodispersity. In my research I am modulating all those three parameters. Perfecting silver nanoparticles synthesis methods [2] allows for obtaining many structures by using various liquid crystal ligands. Type of spatial distribution of nanoparticles is determined by small angle X-ray radiation (SAXS) and transmission electron microscopy (TEM) techniques, while optical properties of the materials are analyzed by UV-Vis spectroscopy.

The research is conducted under Reinforce project carried out within the
First Team programme of the Foundation for Polish Science co-financed by
the European Union under the European Regional Development Fund.

1. Lewandowski W., Fruhnert M., Mieczkowski J., Rockstuhl C., Górecka E. Dynamic self-assembled silver nanoparticles as a thermally tunable metamaterial // Nat. Commun.-2015.-6.
2. Lin L., Chen M., Qin H., Peng X. P. Ag Nanocrystals with Nearly Ideal Optical Quality: Synthesis, Growth Mechanism and Characterizations // J. Am. Chem. Soc.-2018.-140(50),-P. 17734-17742.