Physico-Chemical nanomaterials science

Utilization of char obtained from olive pomace co-pyrolysis with crude oil as a filler in epoxy composite materials

Elif Yilmaz1, Gulcihan Guzel Kaya2, Yakup Kar3, Huseyin Deveci4
1,2,4 Selcuk University, Engineering Faculty, Department of Chemical Engineering, Konya, Turkey, hdeveci@selcuk.edu.tr
3 Iskenderun Technical University, Engineering Faculty, Department of Petroleum and Natural Gas Engineering, Hatay, Turkey.

The usage of coal, biomass, petroleum residue, waste plastic materials etc. with many thermal processes such as co-combustion, co-pyrolysis or co-gasification has attracted great attention taking into account economical and environmental aspects [1]. Co-pyrolysis of biomass is generally chosen due to its simplicity and effectiveness for production of several types of fuels with by-products including liquid, char and gas. Among the by-products, char which has rich carbon content and highly porous strucuture is used in many applications [2]. In the olive oil production processes, olive pomace is obtained as a waste (2x105 tons/year in Turkey) in different stages of conversion of olive to oil. So, recycling of the biomass with different technologies becomes significant when considering problems on environment and human health. In this study, char was obtained from olive pomace co-pyrolysis with crude oil in fixed bed pyrolysis system at 500 °C with a heating rate of 10 °C/min under N2 atmosphere. Subsequently, the char with different weight ratios was used as filler in epoxy resin. Crystal and morphological structure of the composite materials were investigated with XRD and SEM analyses, respectively. Decomposition temperatures of the composite materials were determined with TGA analysis. Tensile strength and hardness tests were performed according to ASTM Standards. Additionally, the contact angle measurements were carried out for each composite material. This study provides a decrease in environmental pollution with the recycling of waste in addition to production of low-cost materials.

References
1. Abnisa, F. and Ashri Wan Daud, W.M. "A review on co-pyrolysis of biomass: An optional technique to obtain a high-grade pyrolysis oil" Energy Conversion and Management, 87 (2014): 71-85.
2. Haykiri-Acma, H. and Yaman, S. "Synergy in devolatilization characteristics of lignite and hazelnut shell during co-pyrolysis" Fuel, 86 (2007): 373-380.